## Slide 1
TECHNICAL TEST SUBMISSION BADARUZZAMAN NAFIZ
Greenhouse IoT
Backend
FastAPI
Reliable sensor ingestion and acknowledged device control through one production-oriented backend.
Mosquitto
PostgreSQL
Docker Compose + Pytest

## Slide 2
Three behaviors define success
The scope stays deliberately small and reviewable.
Validate the payload, preserve recorded_at, and persist the reading in PostgreSQL.
POST /sensor-data
Accept device_id plus ON/OFF and publish a structured command through MQTT QoS 1.
POST /device-control
Probe the backend, SELECT 1 against PostgreSQL, and report the live MQTT connection state.
GET /status
1
2
3
Deliverables
Source code · README · Design explanation · Presentation PDF

## Slide 3
IOT / Clients
FastAPI
PostgreSQL
Mosquitto
Devices
two transport
responsibilities
Requirement interpretation
The implementation contract explicitly makes /sensor-data an HTTP endpoint, while MQTT is reserved for outbound device commands.
HTTP JSON
SQLAlchemy
MQTT QoS 1
One backend,

## Slide 4
sensor_readings | sensor_readings | sensor_readings | sensor_readings | sensor_readings | sensor_readings
id | device_id | created_at | temprature | recorded_at | humidity
PK | text | backend time | numeric | sensor time | 0-100
The contract is explicit before implementation
Validate and persist a reading
POST /sensor-data
Validate and publish a command
POST /device-control
Probe live dependencies
GET /status
1
2
3

## Slide 5
HTTP request
HTTP request
HTTP request
HTTP request
HTTP request
Mosquitto
broker ACK
{ "device_id": "fan-001", "command": "ON",
"timestamp": "2026-09-19T10:35:00Z" }
Persistent MQTT
keeps commands reliable
The HTTP request returns only after publish acceptance is confirmed.
HTTP request
device_id + ON/OFF
DeviceService
builds command
MQTT client
lifecycle-owned
Device
subscribed topic
Topic
greenhouse/control/{device_id}
Payload
Why QoS 1
Broker acknowledgement matters more for control commands than for best-effort telemetry. QoS 1 gives at-least-once delivery, so devices should treat commands idempotently.

## Slide 6
HTTP request
Health is derived from real dependency checks
Failures are visible without exposing credentials or stack traces.
Backend - Up
Database - Connected
MQTT - Conncected
Healthy
Any failed DB query or disconnected MQTT client changes the aggregate status.
Degraded
Consistent error envelope
{
"success": false,
"error": {
"code": "MQTT_UNAVAILABLE",
"message": "MQTT broker is unavailable"
}
}
Malformed JSON, validation failures, database outages, and broker outages follow the same external structure. Internal detail stays in logs.

## Slide 7
Database persistence evidence | Database persistence evidence | Database persistence evidence | Database persistence evidence | Database persistence evidence
id | humidity | stored through | temperature | device_id
2 | 62.8 | POST /sensor-data | 29.4 | reviewer-sensor
Testing proves
the critical paths
Automated tests are paired with manual reviewer-style verification.
/ 21 tests passing
21
Sensor validation · command validation · MQTT failure · healthy/degraded status
MQTT subscriber evidence
$ mosquitto_sub -t greenhouse/control/# -v
greenhouse/control/fan-001
{"device_id":"fan-001","command":"ON",...}
Manual integration run retained separate recorded_at and created_at values.

## Slide 8
Design choices keep the submission focused
Production expansion is possible without hiding today’s failure modes.
Typed validation and automatic OpenAPI with a small code surface.
Current decisions
FastAPI
Durable relational storage with explicit schema evolution.
PostgreSQL + Alembic
Lower request overhead and broker acknowledgement for commands.
Persistent MQTT + QoS 1
Partial failure is surfaced as degraded instead of masked.
Dependency-aware health
TLS, authentication, secret management, and per-device authorization.
Future improvements
Security
Metrics, tracing, structured log aggregation, and alert thresholds.
Observability
Connection tuning, idempotency keys, and horizontal backend replicas.
Scale
Add inbound MQTT consumption only when product requirements demand it.
Telemetry evolution